## Slide 1: RoboRebound: Multi-Robot System Defense with Bounded-Time Interaction
Neeraj Gandhi, Yifan Cai, Andreas Haeberlen, Linh Thi Xuan Phan

## Slide 2: What is a Multi-Robot System?
Hundreds of robots packing orders in grocery warehouses
Cooperating robots map outdoor setting with no GPS
Ocado Warehouse
Impacted industries
Logistics, agriculture, aerospace, outer space, mining, and construction, among others
Common features
Independently mobile robots are ‘nodes’
Communication is over a dynamic, unreliable, wireless network
Wide variety of applications and environments in which systems are deployed

## Slide 3: Faults Can Cause Immense Damage
One robot out of hundreds had a fault
and cost Ocado £100M
Many systems susceptible to
faults that can cause this much damage!

## Slide 4: Problem Overview
With only a few robots, adversaries can disrupt entire system
No Fault
Fault with No Protection
Goal: Develop a technique that can, in bounded time, detect and recover from Byzantine attacks on the robots of a Multi-Robot System

## Slide 5: Approach
Robots audit one another’s logs
Add a tiny bit of trust to each robot
Log
Log
Audit
Audit

## Slide 6: Approach
Robots audit one another’s logs
Add a tiny bit of trust to each robot
Trusted hardware enables tamper-evident logs
Log
Log
Audit
Audit

## Slide 7: What is fault tolerance in mobile robots?
Other approaches to fault tolerance exist
  May not be designed for cyber-physical systems
  May not be designed for dynamic, unreliable networks
  Robots pose a physical threat to one another
Solution: Bounded-time interaction (BTI)
  A faulty robot can only interact with other robots for bounded-time before it is put into “Safe Mode”
Challenge

## Slide 8: Sensors and actuators are local to the robot
Only the on-robot compute node has access to the robot’s sensors and actuators
Threat: A faulty compute node can manipulate sensor data and control vectors
Solution: Tiny, trusted nodes ensure auditability of all messages, including sensor data and control vectors
  TrInc [NSDI’09] showed that small trusted hardware can be used to:
  Create tamper-evident logs of messages
  Reduce communication overheads
Challenge

## Slide 9: Outline
Problem & Challenges
Solution Sketch
Design
Evaluation

## Slide 10: RoboRebound inspiration: Arcades
Add coins to arcade game to extend play time

## Slide 11: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 12: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 13: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 14: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 15: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 16: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 17: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 18: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 19: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 20: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits

## Slide 21: Key idea #1: Bounded-time interaction
Each robot is periodically audited by neighbors
unique tokens to be periodically obtained from successful audits
Game
Over

## Slide 22: Key Idea #2: A little trust for tamper-evident logging
Each robot's computing architecture has:
  Two small trusted nodes ("sensing" and "actuating")
  One large, untrusted node
Sensor
Compute Node
Actuator
Sensor Node
Actuator Node

## Slide 23: Key Idea #2: A little trust for tamper-evident logging
Each robot's computing architecture has:
  Two small trusted nodes ("sensing" and "actuating")
  One large, untrusted node
Sensor
Compute Node
Actuator
Sensor Node
Actuator Node

## Slide 24: Components of RoboRebound
Trusted nodes maintain a hash chain to verify message correctness, existence, and ordering
Trusted nodes provide cryptographically verifiable authenticator to prevent forging of hash chains
All audit requests must include authenticators from trusted nodes
Auditors perform deterministic replay of tamper-evident logs
Successful audits result in auditor issuing a token (robots need tokens)

## Slide 25: Data Flow
Sensor
Sensor Node
Compute Node
Actuator Node
Actuator
Radio
Log
Remote Robot
Hash Chain
Authenticator

## Slide 26: Data Flow
Sensor
Sensor Node
Compute Node
Actuator Node
Actuator
Radio
Log
Remote Robot
Hash Chain
Authenticator
Token

## Slide 27: Outline
Problem & Challenges
Solution Sketch
Design
Evaluation

## Slide 28: Implementation
Simulator in Network Simulator 3 (ns-3)
  End-to-end and scalability experiments
SecBot hardware platform
  Untrusted node: 4-core TinkerBoard S
  Trusted nodes: 1-core PIC32
  Used for microbenchmarks

## Slide 29: Evaluation Questions
Will tiny, trusted nodes work in real hardware?
  - Microbenchmark: CPU Utilization
  - Microbenchmark: IO Overhead
What are the costs of RoboRebound?
  Bandwidth & storage as functions of:
  - Number of faults
  - Time-bound for Bounded-Time Interaction
How effective is RoboRebound?
  Case study
How does RoboRebound scale?
  Bandwidth & storage as functions of:
  - Number of robots
  - Robot spatial density

## Slide 30: Case study: One compromised robot among 25
No Attack
No Defense
Defended

## Slide 31: Overheads in real hardware
Benchmarked SHA-1 & LightMAC on PIC32 microcontroller @ 50MHz
  = 4s
  Wireless state exchange T = 1.5s
  Control period T = 0.25s
  Each robot has ten neighbors
Sensor node core utilization: 5.99%
Actuator node core utilization: 17.28%
Computational overhead is manageable, even on resource-limited embedded systems.

## Slide 32: Scalability as a function of density
16 Robots
36 Robots
100 Robots
64 Robots
16 Robots
36 Robots
100 Robots
64 Robots
Higher density = More neighbors to track
Scales indefinitely at low enough density
Greater spatial density
Greater spatial density

## Slide 33: Conclusion
Problem: Handling faults in MRS requires dealing with the ‘physical’ part of cyber-physical systems and network dynamism + unreliability
Goal: Return a multi-robot system to correct behavior within bounded time
Approach: Bounded-time interaction (BTI)
  RoboRebound provides BTI from faults in robots in a dynamic, unreliable network
  Requires adding two small trusted nodes to make actions auditable
  Robots need to acquire tokens from auditors to continue operating
SecBot is the first BTI-enabled hardware platform
Evaluation: SecBot & ns-3 simulator
  SecBot: Microcontrollers can handle BTI load
  ns-3: Overall overheads are manageable, even at scale
Thank you!

## Slide 34: BW + Storage as functions of flock size

## Slide 35: BW + Storage as functions of f_max, round length

## Slide 36: Assumptions
Network is dynamic and unreliable
Inter-robot space large enough that a crash will not happen in the safe time bound
Lightweight cryptography is usable (Hash, MAC)
Adversary cannot modify circuit boards in robots

## Slide 37: Implementation: SecBot
Designed a BTI-capable robot for robotics research
  4-core TinkerBoard S as the untrusted, complex node
  1-core PIC32 microcontrollers for trusted nodes

## Slide 38: Implementation: SecBot Circuit Board
Two DC motors
Four sensors:
  GNSS, IMU, 2 Encoders
Integrated radio
BTI option
Optional EEPROMs
Motor Driver & Opto-Isolators
Motor Connectors
Battery
Conn.
Optional Common Ground
Power Distribution & Regulation
TinkerBoard Connector
GNSS
IMU
Enc
Actuator Node
Sensor Node
Radio
Antenna
EEPROM
EEPROM

## Slide 39: SecBot Microbenchmarks: Runtime & IO
Hash: SHA1, MAC: LightMAC
SHA-1
LightMAC
Input
Output
We can use these microbenchmarks to extrapolate total overheads for running a BTI system
= 4s
Wireless state exchange T = 1.5s
Control period T = 0.25s
Each robot has ten neighbors
Sensor Node Core Utilization: 5.99%
Actuator Node Core Utilization: 17.28%